# Resolution:
-Chapter name [text]
-Register Used [text]
-Register Picture [picture] / Used Part [picture]
-Description, Instructions and Examples
# Chapter 1: Activate global interrupts

Register Used: SREG
Register Picture:

Instructions: Set bit 7 to 1 to activate the interrupts.
Example: SREG |= 0B10000000;

Notes: alternatively, you may use sei(). from <avr/interrupt.h> library.
Example: sei(); //set external interrupt. It sets the I-bit in the Status Register. [Datasheet page 111, Bit 2 ]

# Chapter 2: Select interrupt mode

Register Used: TCCR0A
Similar: TCCR1A
Register Picture:
Used part:

WGM02 position:

### CTC mode
Description: On Clear Timer on Compare, The counter value (TCNT0) increases until a compare match occurs between TCNT0 and OCR0A, and then counter (TCNT0) is cleared. [Same with TCNT1 and OCR0B, OCR1A, OCR1B]
Instructions: Set the OCR0A to a value of Total Timer Ticks, using the calculator: https://eleccelerator.com/avr-timer-calculator/.

Example of 1 second interrupt:

1) Set System Clock Frequency of yout Atmel mcu.

2) Set the Prescaler, usually to 1024

3) Set the Real Time lets say to 0.01

4) Click on ...Real Time button, and copy the Total Timer Clicks Result. In this case, its 156.25 . You need to round it up, to 156.
Example: OCR0A = 156;

Set the timer on CTC: TCCR0A = (1 << WGM01); //CTC mode (Clear Timer on Compare)

## Chapter 3: Set prescaler
Register Used: TCCR0B

Used Part:

Example: TCCR0B |= (1 << CS02) | (1<< CS00); //1024 prescaler set

Instructions: Use the prescaler that you used on the chapter 2

## Chapter 4: Enable specific interrupt.

Register Used: TIMSK0 [Timer Mask 0]

Register Picture:

On TIMSK0, you can enable OCIE0A or OCIE0Β. These, are specific timers.

Examples:	TIMSK0 = (1 << OCIE0A); //enable OCIE0A in TIMSK0 interrupt

## Chapter 5: Interrupt Routine

When a timer interrupt is activated, it will lead itself into a routine. Using the interrupts library, you make these routines. Its name shall be ISR(){}
And as a parameter, it may contain TIMERx_COMPx_vect, where ‘x’ is the timer name. For example,

for timer B using TIMSK0 :

TIMSK0 = (1 << OCIE0B);
ISR(TIMER0_COMPB_vect) {}

for timer A using TIMSK0 :

TIMSK0 = (1 << OCIE0A);
ISR(TIMER0_COMPA_vect) {}

written
Counter Resolution: The minimum time a counter takes to reach from Bottom value to TOP value.

OCR = Output Compare Register
TCNT = Timer Counter

Τι κανουν αυτα;